## Slide 1: USING ELECTRICITY Chapter #11

## Slide 2: 11.1 Work, Energy and Power

## Slide 3: Work, Power & Energy
Work (W) is defined as the transforming or converting of energy.
  It is measured in joules (J).
An object has energy (E) if it has the ability to do work.
Energy is classified into two major types:
  Potential Energy (PE) is energy that can be stored in an object.
    E.g. gravitational, nuclear, chemical, elastic, magnetic
  Kinetic Energy (KE) is the energy that an object has because of its motion. It depends on both the mass and speed of an object.
    E.g. electrical, light, sound, thermal, wind, mechanical
Therefore, work is equal to the change in energy.

## Slide 4: Work, Power & Energy
All types of energy can be converted from one type to another with no overall loss of energy.
This is the basis for the Law of Conservation of Energy which states that in any closed system, the total amount of energy (including potential energy) remains constant.
Power (P) is the rate at which energy is transformed or the rate at which work is done.
  It is measured in watts (W).

## Slide 5: 11.2 Electrical Energy and Power

## Slide 6: POWER (P)
Electrical power is a measure of the rate at which electrical energy is transformed into other forms of energy.
Electrical power can be calculated using the formula:
  Power (watts) = Energy (joules) Time (seconds)
E
P t

## Slide 7: Example #1
What is the power of a toaster that converts 24 000 J of electrical energy into heat energy in a time of 35 s?
P = E = 24000 J = 685 .7 W
t 35 s
E
P t

## Slide 8: POWER (P)
Electrical power can also be calculated using the formula:
  Power (watts) = voltage (V) x current (A)
P
V I

## Slide 9: Example #2
A 37 W cordless drill uses a current of 2.6 A. What is the voltage of the battery?
P = VI
V = P = 37 W = 14.23 V
I 2.6 A
P
V I

## Slide 10: POWER & ENERGY
Combining the two equations for power give us an equation that allows us to solve for time:
      Energy (joules) = voltage (V) x current (A) x time (s)
E
V I t

## Slide 11: Example #3
A light bulb has a current of 0.5 A when it is connected to a 120 V household outlet. If the light is left on for 30minutes, how much electrical energy is used by the bulb?
E = VIt
= (120 V)(0.5 A)(1800 sec)
= 108,000 J
E
V I t
1800 sec.

## Slide 12: 11.4 Household Electrical Energy

## Slide 13: Electricity
Electric meters measure and record the energy used.
Electric companies don’t charge for power, they charge for the amount of energy used.

## Slide 14: Electric meter Dials
Electric meters are read by alternating between clockwise (cw) and counterclockwise (ccw)
This example reads 08925 kWh

## Slide 15: Example #4
What does the meter read?
43231 kWh

## Slide 16: POWER, ENERGY & COST
To determine energy used, you need to keep track of numbers for 2 dates and then subtract.
To determine cost, multiply energy used by the rate charged by the power company.
The joule is a very small unit so electric companies use the kilowatthour (kWh) instead.
To convert from W  kW ( 1000)
To convert from s  h ( 3600)

## Slide 17: Example #5
The meter reading on June 1st was 84502 kWh. On July 1st , the meter read 87498 kWh. If the cost of electricity in the area was $0.12 per kWh, what was the electric bill for the month of June?
87498
- 84502
2996 kWh x $0.12 = $359.52

## Slide 18: Example #6
A meter reader determines that a business has used 2668 kW⋅h of energy in two months. If electricity costs 12¢ per kW⋅h, calculate the bill.
kW⋅h x cost
2668 kW⋅h x 0.12
= $320.16

## Slide 19: Energuide Labels
Provides information about an appliances electrical energy consumption and efficiency.
Estimates typical energy used (kWh) in a year.
Compares appliances with similar models.
The lower the number, the more efficient the appliance

## Slide 20: Example #7
A toaster is used an average of 5.0 h a month. The toaster draws 8.0 A of current from a 110 V outlet. If electricity costs 8¢ per kW⋅h, how much will it cost to operate the toaster for one year?
P = VI
=(110V) (8 A) = 880 W = 0.88 kW
COST = (0.88 kW) (5h x 12)( $ 0.08 )
= $4.22