## Slide 1: Voltage

## Slide 2: Voltage (V)
Electrical energy is carried through a circuit by electrons.
In a circuit, we can measure the change in potential energy between two different points on the circuit, and we call this potential difference, or voltage (V).
The voltmeter is always connected across the device (parallel)
Reminder: this is to measure the difference between 2 points

## Slide 3
Voltage is measured in volts (V).
Voltage is measured by a device called a voltmeter
Ex. a AA or AAA battery has a potential difference of 1.5 V between its two ends, so we call it a 1.5 V battery.

## Slide 4: SERIES and PARALLEL
In a circuit, devices such as light bulbs or batteries can be placed in two different ways.
SERIES
PARALLEL

## Slide 5: Calculating Voltage in SERIES
When cells are connected in series, we can find the total amount of voltage by just adding them together.
VT = V1 + V2
V1
V2
VT

## Slide 6: Example #1
What is VT?
VT = V1 + V2 + V3 + V4
VT = 10 + 35 + 45 + 20
VT = 110 V

## Slide 7: Calculating Voltage in Parallel
When cells are combined in parallel, the voltage does not increase but the amount of charge (current) does.
  Refer to Figure 10 (p. 313)
Advantages: greater current or longer battery life
VT = V1 = V2 = V3
VT
V1
V2
V3

## Slide 8: Example #2
Calculate VT , V2 , V3
VT = V1 = V2 = V3
= 9 V
VT
9 V
V2
V3

## Slide 9
Type of Circuit | Series | Parallel
Total Current (IT) | IT = I1 = I2 = I3 | IT = I1 + I2 + I3
Total Voltage (VT) | VT = V1 + V2 + V3 | VT = V1 = V2 = V3